## Slide 1: EECE 229 Introduction to Digital Systems

## Slide 2: Chapter 2
Boolean Algebra and Logic Gates

## Slide 3: Boolean Algebra
The algebraic system usually used to work with binary logic expressions.
1. Closure | Any defined operation on (0, 1) gives (0,1) | 
2. Identity: | 0 + x = x ; | 1 . x = x
3. Commutative: | x + y = y + x ; | xy = yx
4. Distributive: | x (y + z) = xy + xz; | x + (yz) = (x + y)(x + z)
5. Def of Complement: | x + x’ = 1; | x x’ = 0
6. At least 2 elements (0 and 1) |  | 

## Slide 4: The Duality Principle
Examples:
x + x’ = 1
so: xx’ = 0
x + y = y + x
so: xy = yx
Given a logic expression, its dual is obtained by replacing all + operator with . operator, and vice versa, and by replacing all 0s with all 1s, with versa.

## Slide 5: Useful Postulates and Theorems
 | (a) | (b)
Postulate 2 | x + 0 = x | x . 1 = x
Postulate 5 | x + x’ = 1 | xx’ = 0
Theorem 1 | x + x = x | xx = x
Theorem 2 | x + 1 = 1 | x .0 = 0
Theorem 3 (involution) | (x’)’ = x | 
Postulate 3 (commutative) | x + y = y + x | xy = yx
Theorem 4 (associative) | x + (y + z) = (x + y) +z | x(yz) = (xy)z
Postulate 4 (distributive) | x(y + z) = xy + xz | x + yz = (x + y)(x + z)
Theorem 5 (deMorgan’s Law) | (x + y)’ = x’y’ | (xy)’ = x’ + y’
Theorem 6 (absorption) | x + xy = x | x (x + y) = x

## Slide 6: Proving the Theorems
Theorem 1: x + x = x; xx = x
Proof:
x + x
= (x + x) 1
postulate
2(b)
= (x + x)(x + x’)
5(a)
= x + xx’
4(b)
= x + 0
5(b)
= x
2(a)
xx = x by duality

## Slide 7: Proving by Truth Table
Two Boolean expressions are equal in all cases if and only if they have the same Truth Table.
You may use this to prove the expressions are equal.

## Slide 8: Proving by Truth Table
Example: Prove deMorgan’s Law: (x + y)’ = x’y’
The Truth Table of (x + y)’ is equal to
the Truth Table of x’y’, so we know that
(x + y)’ = x’y’
for all values of x and y.
x | y | (x + y) | (x + y)’ | x’ | y’ | x’y’
0 | 0 | 0 | 1 | 1 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 9: Boolean functions and circuit equivalents

## Slide 10: Implementing a Boolean expression as a circuit
F1 = x + y’z
x
y’z
F1
F1
x
y’ z
F1
x
z
y’z
y’z
y’
y

## Slide 11: Simplifying expressions
There are many different ways to write the same expression
  Example: x’y’z’ + x’yz + xy’ = xy’ + x’z
Different forms of the expression will require different numbers of gates to implement
Generally, longer expressions with more terms require more gates and/or more complex gates
  More gates : higher power, higher cost, larger size, …
So finding a way to simplify expressions will pay off in terms of the circuits we design

## Slide 12: A metric for use in simplifying expressions
Define a “literal” as each occurrence of a variable in the expression:
– Example: F2 = x’y’z + x’yz + xy’  8 literals
If we can write the expression with fewer literal, we will consider it to be simpler (and to take fewer gates).
Note that this is a rule of thumb and does not always give an optimum answer.

## Slide 13: Simplifying expressions using the postulates and theorems of Boolean Algebra
1. x(x’ + y)
= xx’ + xy
= 0 + xy
= xy
p4a p5b p2a
2. x+x’y
= x+y (the dual of 1)

## Slide 14: Simplifying expressions using the postulates and theorems of Boolean Algebra
3. (x+y)(x+y’) = x + yy’
= x+0
= x
p4a p5b p2a

## Slide 15: Complementing a function
(x + y)’ = x’y’
deMorgan’s Law says:
To take (A + B + C)’ Let y = B+C
Then
(A + B + C)’ = (A + y)’ = A’y’ = A’(B + C)’ = A’B’C’
In general:
(A+B+C+D+…)’ = A’B’C’D’… ;
(ABCD…)’ = A’+B’+C’+D’…
A more complex function:
F = x’yz’ + x’y’z
F’ = (x’yz’ + x’y’z)’
= (x’yz’)’(x’y’z)’
= (x + y’ + z)(x + y + z’)

## Slide 16: Another way: complementing a function
To complement a function, you can take the dual of the function, and complement each literal.
For the previous example:
F
= x’yz’ + x’y’z
dual of F
= (x’ + y + z’)(x’ + y’ + z)
so F’
= (x + y’ + z)(x + y + z’)

## Slide 17: Standard forms of Boolean Expressions

## Slide 18: Definitions
Product term
a term consisting of literals ANDed together
» Example: AB’F
Minterm
a Product term in which all variables appear
» Example: ABC’D where A,B,C, and D are the variables of the function
Sum term
a term consisting of literals ORed together
» Example: A + B’ + F
Maxterm
a Sum term in which all variables appear
» Example: A + B + C + D where A, B, C, and D are the variables of the function

## Slide 19: SOP and Canonical SOP Form
A function is in Sum of Products (SOP) form if it is written as product terms ORed together
– Example: f(x y z) = xy’z + xz + y
A function is in Canonical SOP form if it is in SOP form and all terms are minterms
– Example: g(x y z) = xy’z + x’yz + xyz

## Slide 20: POS and Canonical POS form
A function is in Product of Sums (POS) form if it is written as sum terms ANDed together
– Example: f(x y z) = (x + y + z) ( x + z’) (y)
A function is in Canonical POS form if it is written in POS form and all terms are Maxterms
– Example: g(x y z) = (x’ + y’ + z’) ( x + y + z)

## Slide 21: Three-variable minterms and maxterms

## Slide 22
Three-variable minterms and maxterms

## Slide 23: Minterms and the Truth Table
Each row of a Truth Table corresponds to a minterm.
The 1’s of the Truth Table show the minterms that are
in the Canonical SOP expression
Minterm List Form: f(x y z) =
m(1, 4, 5, 7)
x | y | z | f(x y z) |  | minterm
0 | 0 | 0 | 0 |  | x’ y’ z’
0 | 0 | 1 | 1 | m1 | x’ y’ z
0 | 1 | 0 | 0 | m2 | x’ y z’
0 | 1 | 1 | 0 | m3 | x’ y z
1 | 0 | 0 | 1 | m4 | x | y’ z’ | 
1 | 0 | 1 | 1 | m5 | x | y’ z | 
1 | 1 | 0 | 0 | m6 | x | y z’ | 
1 | 1 | 1 | 1 | m7 | x | y z | f(x y z) = x’y’z + xy’z’ + xy’z + x y z
m0
Row numbers

## Slide 24: Examples
f(x y z)
= x’y’z + xy’z’ + xyz
=
A B C D
g(ABCD)
g(A B C D) = A’B’C’D + AB’CD’ + ABC’D
=
x | y | z | f(xyz)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0

## Slide 25: Maxterms and the Truth Table
x y z f(x y z) Maxterm
The 0’s of the Truth Table show the maxterms that are
in the Canonical POS expression
Maxterm List Form: f(x y z) =
M(0,3,6)
Note the differences from the way minterms are complemented
0 | 0 | 0 | 0 | M0 | x | + y + z
0 | 0 | 1 | 1 | M1 | x | + y + z’
0 | 1 | 0 | 1 | M2 | x | + y’ + z
0 | 1 | 1 | 0 | M3 | x | + y’ + z’
1 | 0 | 0 | 1 | M4 | x’ + y + z | 
1 | 0 | 1 | 1 | M5 | x’ + y + z’ | 
1 | 1 | 0 | 0 | M6 | x’ + y’ + z | 
1 | 1 | 1 | 1 | M7 | x’ + y’ + z’ | f(x y z) = (x+y+z)(x+y’+z)(x’+y’+z)
Each row of a Truth Table corresponds to a maxterm.

## Slide 26: Example
f(x y z) = (x+y+z)(x+y’+z)(x+y’+z’)(x’+y+z’)(x’+y’+z)
=
Note that the Minterm List and Maxterm List taken together include the number of every row of the Truth Table. That means that if you determine either one of the lists, you can determine the other one by simply writing the row numbers that are not in the first one.
Examples:
If F(ABC) = m(0-3), then F(ABC) = M(4-7)
if G(wxyz) = M(0,12,15), then G(wxyz) = m(1-11, 13, 14)
x | y | z | f(xyz)
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 27: Basic Combinational Circuit Designs

## Slide 28
A binary switch.
x
1
=
x
0
=
(a) Two states of a switch
S
x
(b) Symbol for a switch
Review: Digital Logic Gates

## Slide 29
A light controlled by a switch
Power
supply
S
Light
x
Consider a simple application of a switch, where the switch turns a small lightbulb on or off.
Describe the state of light as a function of the input variable x. L=1, if x=1. L=0, if x=0.
L(x) = x
Review: Digital Logic Gates

## Slide 30
(a) The logical AND function (series connection)
S
Power
supply
S
S
Power
supply
S
(b) The logical OR function (parallel connection)
Light
Light
x1
x2
x1
x2
Notes: L=X1+X2; X1=1, X2=1, L=1
L=X1*X2; X1=1, X2=0, L=1;

## Slide 31
An inverting circuit
S
Light
Power
supply
R
x
Review: Digital Logic Gates
An extra resister to ensure that the closed switch does not short-circuit the power supply.
Notes: L=x’ x=1, L=0; x=0, L=1;

## Slide 32
A
F = A’
0
1
1
0
A B
F = AB
0
0
0
1
0
0
1 0
0
1
1
1
A B
F = A+B
0
0
0
1
0
1
1 0
1
1
1
1
NOT
AND
OR
Review: Digital Logic Gates

## Slide 33
Three-input AND and OR operations.
Review: Digital Logic Gates

## Slide 34
x
1
x
2
x
n
x
1
x
2
¼
x
n
+
+
+
x
1
x
2
x
1
x
2
+
x
1
x
2
x
n
x
1
x
2
x
1
x
2
×
x
1
x
2
¼
x
n
×
×
×
(a) AND gates
(b) OR gates
x
x
(c) NOT gate

## Slide 35
Review: Digital Logic Gates

## Slide 36: SOP to “AND-OR”
An SOP expression can be directly implemented in a two-level combinational circuit with an AND gate for each product term and an OR gate to combine the terms.
Example:
f(xyz) = x + x’y + x’y’z
x
x’
y
x’
y’ z
f(xyz)

## Slide 37: POS to “OR-AND”
A POS expression can be directly implemented in a two-level combinational circuit with an OR gate for each sum term and an AND gate to combine the terms.
Example:
f(wxyz) = z’(x+y)(w+z)
x y
w z
f(wxyz)
z’

## Slide 38: Circuits for mixed-form expressions
Combinational circuits for mixed-form expressions may have more than two levels.
Example:
f(ABCDE) = AB + C(D + E)
A B C
D E
f(ABCDE)

## Slide 39: Other common gate types
x y
(xy)’ = x’ + y’
NAND
x
y
(x+y)’ = x’y’
NOR
Exclusive-OR (XOR)
x y
xy’ + x’y
= x + y
x y x NAND y
1
1
1
0
x y x NOR y
0 0
0 1
1 0
1 1
1
0
0
0
0 | 0
0 | 1
1 | 0
1 | 1
x | y | x | XOR y
0 | 0 |  | 0
0 | 1 |  | 1
1 | 0 |  | 1
1 | 1 |  | 0

## Slide 40: AND, OR, and NOT Convert to NAND and NOR
x
(xx)’ = x’
((xy)’)’ = xy
x y
x
y
(x’y’)’ = x+y
x
(x+x)’ = x’
x y
((x+y)’)’ = x+y
x
y
(x’+y’)’
= x’’y’’
= xy
NOT
AND
OR

## Slide 41: SOP to NAND (1)
x
x’ y
f(xyz)
x’
y’ z
x’
y’ z
We can substitute the NAND equivalents for the AND and OR gates x
x’ y
We already determined that we can go directly from SOP form to an AND-OR implementation
f(xyz) = x + x’y + x’y’z
f(xyz)

## Slide 42: SOP to NAND (2)
x’
y’ z
f(xyz)
x’
y’ z
f(xyz)
The circled gates are just 2 inverters in series – they do nothing
x
x’ y
So leave them out
x
x’ y

## Slide 43: SOP to NAND (3)
x’
y’ z
f(xyz)
x
x’ y
Check: Is this still the original f(xyz)?
The circuit produces:
(x’(x’y)’(x’y’z))’ = x’’ + (x’y)’’ + (x’y’z)’’ = x + x’y + x’y’z

## Slide 44: SOP to NAND (4)
We can use NAND gates to directly implement any SOP expression:
      One NAND for each Product term
      One NAND to sum the terms
      Invert any single inputs
Why do we do this?
      The NAND integrated circuit design is very simple.
      We can use this one simple gate type for any expression.

## Slide 45
x
1
x
2
x
3
x
4
x
5
x
1
x
2
x
3
x
4
x
5
x
1
x
2
x
3
x
4
x
5
Using NAND gates to implement a sum-of-products

## Slide 46
Using NOR gates to implement a product-of sums
x
1
x
2
x
3
x
4
x
5
x
1
x
2
x
3
x
4
x
5
x
1
x
2
x
3
x
4
x
5

## Slide 47: SOP to NAND (5)
Example:
f(A,B,C,D) = A’B + AC + ABD’
A’ B
A
C
A
B
D’
f(A,B,C,D)

## Slide 48: Cascading 2-input NANDs to implement larger NAND functions
Think of a multiple-input NAND as an AND followed by an INVERTER
x y z
x y z
We can easily build a multiple-input AND out of 2-input ANDs
x y z
x y z
And we know how to build a 2-input AND from 2-input NANDs
y z
y z
y
z
Substituting
x
(xyz)’
(xyz)’
xyz
xyz
yz
(yz)’’ = yz
(x (yz)’’)’ = (xyz)’

## Slide 49: Example
Let us implement the function
Using NAND gates only. Hint, first derive sum of product expression.

## Slide 50
f
f
(a) SOP implementation
(b) NAND implementation
x1
x3
x2
x3
x2
x1

## Slide 51: Example
Let us implement the function
Using NOR gates only. Hint, first derive product of sum expression.
)

## Slide 52
NOR-gate realization of the function
x1
f
(a) POS implementation
(b) NOR implementation
f
x3
x2
x1
x3
x2

## Slide 53: Synthesis
The process where by we begin with a description of the desired functional behavior, then generate a circuit that realizes this behavior is called synthesis.
Truth Table -> Logic Expression -> Logic Circuit

## Slide 54: Gate-Level Minimization

## Slide 55: Karnaugh Maps (“K-Maps”)
Based on the Theorem: xA’ + xA = x(A’ + A) = x
This means that two product terms that differ only in one literal (the literal is complemented in one term and uncomplemented in the other) can be grouped to form a single term without that literal. Call terms like this “logically adjacent”.
examples:
w’x’yz + wx’yz = x’yz
ab’ + ab = a
xyz + xy’z + xy’z’ + x’y’z’ = xz + y’z’

## Slide 56: Extending the theorem
The theorem extends to any number of terms that is a power of 2
Notice that all possible combinations of A and B are included here
xA’B’ + xA’B + xAB’ + xAB = xA’(B’ + B) + xA(B’ + B)
= xA’ + xA
= x

## Slide 57: Logically-adjacent minterms
The Karnaugh Map (“K-Map”) is a diagram that arranges the minterms so that if two Minterms are Logically Adjacent, they are physically adjacent in the diagram.
For 3 variables
This gives a convenient way to combine logically-adjacent terms
m0 000 x’y’z’ | m1 001 x’y’z | m3 011 x’yz | m2 010 x’yz’
m4 100 xy’z’ | m5 101 xy’z | m7 111 xyz | m6 110 xyz’

## Slide 58: 2-variable Karnaugh Map
x y
0
1
x | y | f |  |  | 
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 |  |  | 
1 1 | 0 1 | 0 1 | 1 | 0 | 1
x | y | f |  |  | 
0 | 0 | m0 | 0 | m0 | m2
0 | 1 | m1 |  |  | 
1 1 | 0 1 | m2 m3 | 1 | m1 | m3
x y
0
1
m2 + m3 = x’y + xy
=(x+x’)y
= y

## Slide 59: 2-variable Karnaugh Map
x y
0
1
x | y | f |  |  | 
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 |  |  | 
1 1 | 0 1 | 1 1 | 1 | 1 | 1

## Slide 60: Grouping
x y
0
1
1 1
1
0 0
1
We can group 2
adjacent terms on the K-Map.
The resulting term contains those literals that are common to all of the grouped terms.
In the example above, we grouped minterms xy’ and xy
The result is
x

## Slide 61: Grouping
x y
0
1
1 1
1
0 0
1
Note that it’s OK to use a minterm more than once.

## Slide 62: The K-Map produces the same results as algebraic simplification (faster)
x y
0
1
Algebraically:
f(x,y) = x’y + xy’ + xy
= x’y + xy’ + xy + xy
= x’y + xy + xy’ + xy
= (x’+x)y + x(y’+y)
= y + x
f(x,y) = y + x
x | y | f |  |  | 
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 1 |  |  | 
1 1 | 0 1 | 1 1 | 1 | 1 | 1

## Slide 63: 3-variable K-Maps
x
yz
0
1
00 01 11 10
End cells are adjacent
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6

## Slide 64: Example 1
x
yz
0
00 01 11 10
1
1 1
1
1
0
1
3
2
4
5
7
6
f(x,y,z) = xy’ + x’y
f(𝑥,𝑦,𝑧)=∑𝑚(2−5)

## Slide 65: Example 2
x
yz
0
00 01 11 10
1
1 1
1
1
0
1
3
2
4
5
7
6
f(x,y,z) = xz’ + yz
f(𝑥,𝑦,𝑧)=∑𝑚(3,4,6,7)

## Slide 66: Example 3
x
yz
0
1
00 01 11 10
f(x,y,z) = y’ + x’z
0 | 1 | 1 | 1 | 3 1 | 2
4 |  | 5 |  | 7 | 6
 | 1 |  | 1 |  | 
f(𝑥,𝑦,𝑧)=∑𝑚(0,1, 3, 4, 5)

## Slide 67: Mapping SOP expressions onto the K-Map
For each product term, write 1 in every cell that is in the “intersection” of the literals in the term
x
yz
1
0
00 01 11 10
x
yz
1
0
x
yz
1
0
00 01 11 10
x
yz
1
0
x’yz’
xz
x’
yz’
y’ + x’z
00 01 11 10
xy’ + x’z’ + y’z’ 00 01 11 10
0 | 1 | 3 | 2 1
4 | 5 | 7 | 6
0 | 1 | 1 | 1 | 3 1 | 2
4 |  | 5 |  | 7 | 6
 | 1 |  | 1 |  | 
0 | 1 | 3 | 2
4 | 5 1 | 7 1 | 6
0 | 1 | 1 |  | 3 | 2 1
4 |  | 5 |  | 7 | 6
 | 1 |  | 1 |  | 

## Slide 68: Grouping
x
yz
1
0
00 01 11 10
f(x,y,z) = y’ + yz
x
yz
1
0
00 01 11 10
f(x,y,z) = y’ + z
0 | 1 | 1 | 1 | 3 | 1 | 2
4 |  | 5 |  | 7 |  | 6
 | 1 |  | 1 |  | 1 | 
0 | 1 | 1 | 1 | 3 | 1 | 2
4 |  | 5 |  | 7 |  | 6
 | 1 |  | 1 |  | 1 | 
Get simpler expression for bigger grouping

## Slide 69: Grouping
x
yz
1
0
00 01 11 10
f(x,y,z) = y’z’ + xz
x
yz
0
00 01 11 10
1 1
1
0
1
3
2
4
5
7
6
f(x,y,z) = y’z’ + xz + xy’
1
1
0 | 1 | 1 |  | 3 |  | 2
4 |  | 5 |  | 7 |  | 6
 | 1 |  | 1 |  | 1 | 
Must cover all terms, but covering terms more than once increases complexity

## Slide 70: 4 variable K-Maps
wx
yz 00
01
00
01 11 10
11
10
Sides are adjacent
Top and Bottom Are adjacent
Note that
The 4 corners are adjacent to each other
m0 | m1 | m3 | m2
m4 | m5 | m7 | m6
m12 | m13 | m15 | m14
m8 | m9 | m11 | m10

## Slide 71: Grouping
wx
yz 00
01 11 10
00
01
11
10
0 1 | 1 1 | 3 | 2
4 | 5 | 7 | 6
12 | 13 | 15 1 | 14 1
8 | 9 | 11 1 | 10 1
∑𝑚(0,1, 10, 11, 14, 15)

## Slide 72: Crossing the sides
wx
yz 00
01
00
0
1 3 2
4
5
7 6
12
13
8
9
11
10
1
1 1
15 14
1
11 10
1
1
1 1
1
1 1
∑𝑚(0-2, 4-6, 8, 9, 12-14)

## Slide 73: Crossing top and bottom, grouping corners
AB
CD 00
01
00
01 11 10
0
1
3 2
4
5
7 6
12
13
15
14
8
9
11
10
11
10
1
1 1
1
1
1 1
F(A,B,C,D) = A’B’C’ + B’CD’ +A’BCD’ + AB’C’
F(A,B,C,D) = B’C’ + B’D’ + A’CD’

## Slide 74: Complementing with K-Maps
wx
yz 00
01 11 10
To simplify the complemented expression, group the 0’s
00 | 0 | 1 | 1 | 1 | 3 | 0 | 2 | 0
 | 4 |  | 5 |  | 7 |  | 6 | 
01 |  | 0 |  | 0 |  | 0 |  | 0
 | 12 |  | 13 |  | 15 |  | 14 | 
11 |  | 0 |  | 0 |  | 1 |  | 1
10 | 8 | 0 | 9 | 0 | 11 | 1 | 10 | 1
∑𝑚(0,1, 10, 11, 14, 15)

## Slide 75: “Don’t Cares”
Sometimes we don’t care if a the result of evaluating a Boolean expression for a particular minterm gives a 0 or 1. This often happens because the combination of literals represented by the minterm cannot occur.
Example: f(ABCD)=1 if the BCD digit ABCD is even (not 0)
∑𝑚(2,4,6,8) + ∑d(10-15)

## Slide 76
Consider don’t cares by treating them as if d is 1
AB
CD 00
01
00
01 11 10
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
10
1
1
1
d
1
11 d
d
d
d d
If we treated all don’t cares as 1:
∑𝑚(2,4,6,8) + ∑d(10-15)

## Slide 77
AB
CD 00
01
00
01 11 10
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
10
1
1
1
d
1
11 d
d
d
d d
If we treated all don’t cares as 0:
Consider don’t cares by treating them as if d is 0
∑𝑚(2,4,6,8) + ∑d(10-15)

## Slide 78: The best approach
AB
CD 00
01
00
01 11 10
0
1
3
2
4
5
7
6
12
13
15
14
8
9
11
10
10
1
1
1
d
1
11 d
d
d
d d
treat d’s as 1 where they help make larger groups for the “real” 1’s
treat them as 0 where they do not.
∑𝑚(2,4,6,8) + ∑d(10-15)

## Slide 79: Example
yz
01
wx
00
00 01 11 10
11
10
f(wxyz) = yz + w’x’
yz
01
wx
00
00 01 11 10
11
10
f(wxyz) = yz + w’z
0 d | 1 1 | 3 1 | 2 d
4 | 5 d | 7 1 | 6
12 | 13 | 15 1 | 14
8 | 9 | 11 1 | 10
0 d | 1 1 | 3 1 | 2 d
4 | 5 d | 7 1 | 6
12 | 13 | 15 1 | 14
8 | 9 | 11 1 | 10
∑𝑚(1,3,7,11,15) + ∑d(0,2,5)

## Slide 80: Conclusion
Boolean algebra
Simplify expressions using Boolean algebra (postulates and theorems)
Standard forms of Boolean expressions (Minterms and Maxterms, SOP, POS)
Synthesis (basic circuit designs using SOP or POS)
Using NAND gates/NOR gates to implement SOP/POS
Gate level minimization K-maps (three variables/four variables, don’t cares)