## Slide 1: EECE 229 Introduction to Digital Systems

## Slide 2: Chapter 6
Registers and Counters

## Slide 3: Overview
Registers
  4-bit register
  4-bit shift register
  Serial adder
  Universal shift register
Counters
  Ripple counter
  Synchronous counter

## Slide 4: Registers and Counters
A clocked sequential circuit consists of a group of flip-flops and combinational gates connected to form a feedback path.
Circuits that include flip-flops are usually classified by the function they perform.
Two such circuits are registers and counters.

## Slide 5: registers

## Slide 6: Registers
A register is a group of flip-flops. Each flip-flop is capable of storing one bit of information.
An n-bit register consists of a group of n flip-flops capable of storing n bits of binary information.
A register may have combinational gates that perform data processing task.
The flip-flops holds binary information and the gates determine how the information is transferred into the register.

## Slide 7
4-bit register
A register constructed with four D flip-flops.
The common clock input triggers all flip-flops on positive edge of each pulse, and binary data available at four inputs are transferred into the 4-bit register.
The clear input R, resets inputs of all flip-flops. R=0, the registers are cleared to all 0’s. R=1 is maintained during normal clocked operations.

## Slide 8
4-bit register
The clock must be inhibited from the circuit if the content of the register must be left unchanged.
An enable gate can be used to control the clock input signal.
However, the insertion of logic gates with clock pulses brings propagation delays and may cause system go out of synchronism!
It is advisable to control inputs rather than clock!

## Slide 9
Registers with Parallel Load
Load control input to the register determine the action to be taken with each clock pulse.
If “Load” =1, the register will load from the inputs.
If “Load” =0, the register will hold the stored value by connecting the output of flip-flop to present state.
The load input controls the next clock pulse will accept new information or leave the information in the register intact.
Notice that the register
will load from the inputs
on every clock pulse

## Slide 10
Computer Science
The University Of Alabama in Huntsville
Serial versus parallel load
0 0 1 0 1 1 0 0
Parallel load
0 0 1 0 1 1 0 0
0
0 0
1 0 0
1 1 0 0
After clock pulse 1
After clock pulse 1
After clock pulse 2
After clock pulse 3
After clock pulse 4
Serial load
0 0 1 0 1 1 0 0
0 0 1 0 1 1 0
0 0 1 0 1 1
0 0 1 0 1
0 0 1 0

## Slide 11
4-bit shift register
A shift register consists of a chain of flip-flops in cascade, with the output of one flip-flop connected to the input of the next flip-flop.
Serial input controls what goes into the leftmost flip-flop during the shift.
Serial output controls what goes out from the rightmost flip-flop during the shift.
Shift operation can be controlled through D inputs of the flip-flops.

## Slide 12
Shift registers
The idea
0 0 1 0 0 0 0 0
“right shift”
0 0 0 1 0 0 0 0
“left shift”
0 0 1 0 0 0 0 0
bit ready to
be “shifted in”
0
bit that was
“shifted out”
0
0
1001
Shift left one bit?
10010

## Slide 13: Serial Transfer
A digital system is said to operate in a serial mode when information is transferred and manipulated one bit at a time.
This is in contrast to parallel transfer where all the bits of the register are transferred at the same time.
The serial transfer can be done with shift registers.

## Slide 14
Serial transfer
Serial transfer of information from register A to register B.
The serial output (SO) of register A is connected to serial input (SI) of register B.
SO is connected to SI in register A to prevent information loss.
Each rising edge under shift control (1) will cause a shift in both registers.

## Slide 15
Serial transfer

## Slide 16: Serial Adder
Operations in digital computers are usually done in parallel because this is a faster mode of operation.
Serial operations are slower, but have the advantage of requiring less equipment.
The two binary numbers to be added serially are stored in two shift registers.
Bits are added one pair at a time through a single full adder.

## Slide 17
Serial Adder
Register A holds the augend, and register B holds the addend, the carry flip-flop is cleared to 0.
The carry out of the full adder is transferred to a D flip-flop.
The output of the D flip-flop is then used as carry input for the next pair of significant bits.

## Slide 18: Universal Shift Register
A parallel-load control to enable a parallel transfer and the n input lines associated with the parallel transfer.
n parallel output lines.
A control state that leaves the information in the register unchanged in the presence of the clock.
If the register has both shifts and parallel load capabilities, it is referred to as a universal shift register.

## Slide 19
Universal Shift Register
mode control
S1 S0 Operation
------------------------
0 0 no change
0 1 Shift right
1 0 Shift left
1 1 Parallel load

## Slide 20
S1 S0 Operation
------------------------
0 0 no change
0 1 Shift right
1 0 Shift left
1 1 Parallel load
Operation Diagrams

## Slide 21
S1 S0 Operation
------------------------
0 0 no change
0 1 Shift right
1 0 Shift left
1 1 Parallel load
Active lines for Parallel Load

## Slide 22
S1 S0 Operation
------------------------
0 0 no change
0 1 Shift right
1 0 Shift left
1 1 Parallel load
Active lines for No change

## Slide 23
S1 S0 Operation
------------------------
0 0 no change
0 1 Shift right
1 0 Shift left
1 1 Parallel load
Active lines for Shift Right

## Slide 24
Computer Science
The University Of Alabama in Huntsville
cs309
S1 S0 Operation
------------------------
0 0 no change
0 1 Shift right
1 0 Shift left
1 1 Parallel load
Active lines for Shift Left

## Slide 25: Counters

## Slide 26: Counters
A register that goes through a prescribed sequence of states upon the application of input pulse is called a counter.
A counter that follows the binary number sequence is called a binary counter.
Counters are available in two categories
  Ripple counters
  Synchronous counters

## Slide 27: Counters
Ripple counter
  The flip-flop output transition serves as a source for triggering other flip-flops.
  The C input of some or all flip-flops are triggered not by the common clock pulse.
Synchronous counter
  The C input of all flip-flops receive the common clock.

## Slide 28: Binary Ripple Counter
Consists of a series connection of complementing flip-flops.
The output of each flip-flop is connected to the C input of the next flip-flop in sequence.
The flip-flop holding the last significant bit receives the incoming count pulse.
A complementing flip-flop can be obtained from:
  JK flip-flop with the J and K inputs tied together
  T flip-flop
  D flip-flop with the complement output connected to the D input

## Slide 29
Binary Ripple Counter
In a ripple counter, the clock (count) pulse is applied to the first stage only. The change in stage “n” triggers the clock pulse for stage “n+1”.
FF’s are triggered by a 1->0 transition on the clock input
D input is always the complement of the present state.
T=1, causing the each flip-flop complement the present state.

## Slide 30: Binary Ripple Counter
The least significant bit A0 is complemented with each count pulse input.
Every time that A0 goes from 1 to 0, it complements A1.
Every time that A1 goes from 1 to 0, it complements A2.
Every time that A2 goes from 1 to 0, it complements A3.

## Slide 31: BCD Ripple Counter
A decimal counter follows a sequence of ten states and returns to 0 after the count of 9.
This is similar to a binary counter, except that the state after 1001 is 0000.
The operation of the counter can be explained by a list of conditions for flip-flop transitions.

## Slide 32
Decade Ripple Counter
State Diagram of a Decimal BCD Counter
BCD Ripple Counter

## Slide 33: BCD Ripple Counter
The BCD counter of is a decade counter.
To count in decimal from 0 to 999, we need a three-decade counter.
Multiple decade counters can be constructed by connecting BCD counters in cascade, one for each decade.

## Slide 34: Synchronous Counters
Synchronous counters are different from ripple counters in that clock pulses are applied to the inputs of all flip-flops.
A common clock triggers all flip-flops simultaneously rather than one at a time in succession as in a ripple counter.

## Slide 35
Synchronous Counters
In a synchronous counter
the clock (count) pulse is
applied to all stages at once
4-Bit Synchronous Binary Counter

## Slide 36
Up-Down Counter
4-Bit Synchronous Up-Down Binary Counter
The two operations can be combined in one circuit to form a counter capable of counting up or down.
It has an up control input and down control input.

## Slide 37: Ring Counter
A ring counter is a circular shift register with only one flip-flop being set at any particular time, all others are cleared.
The single bit is shifted from one flip-flop to the next to produce the sequence of timing signals.
The decoder decodes the four states of the counter and generates the required sequence of timing signals.

## Slide 38: Conclusion
Know what is a register
Understand the difference between parallel load and serial load for register
Know circuits of a 4-bit register
Know the 4-bit shift register
Know the serial transfer example
Know universal shift register
Know binary ripple counter and understand the circuits
Know BCD ripple counter and Up-Down counter
Know the difference between ripple counter and synchronous counter

## Slide 39
Reference:
Some of the artwork and graphs are from the following books:
1. Fundamentals of Digital Logic with Verilog design, by Stephen Brown and Zvonko Vranesic, 3rd edition, McGraw Hill
2. Digital Design, 5th Edition, By M. Morris Mano, Michael D. Ciletti, Prentice Hall.